## Slide 1: High Speed Drill calibration A deep learning approach
Clement Wang
clementwang2001@gmail.com
Supervisor: Christian Koch christian.koch@stryker.com

## Slide 2: Summary: I. Problem statement II. Pipeline overview III.2D Key points detection IV. Triangulation V. Future works

## Slide 3: Problem statement
Accelerating instrument calibration
from 2 minutes to 10 seconds

## Slide 4: I. Introduction of the context
Navigation system
FP8000 camera
NIR Cameras
RGB Camera
High speed drill instrument
Track the surgery instruments to ensure safety
Provide guidance during the surgery

## Slide 5: I. Problem definition
3D positions are tracked through tracker-to-tip 3D transformation
Getting this transformation requires manual calibration and is repetitive and time-consuming (up to 2 minutes)
Results of the internship: Accelerate the calibration from 2 minute to 10 seconds

## Slide 6: II. How does it work?
A deep learning based approach

## Slide 7: II. Related Deep learning problems
Key points detection
Semantic ill-defined key points
Research focus on detection rather than accuracy
Depth estimation
Not intended to achieve millimeter-level precision
Requires fully annotated datasets

## Slide 8: II. Pipeline overview
RGB images
2D key points detection
Deep learning based
Triangulation
3D transformation
Annotations come from manual calibration and projection

## Slide 9: III. Diving into key points detection

## Slide 10: III. Basic understanding of Deep learning
Inputs:
512x512 images
Outputs:
Key points coordinates
(2,)
Neural network
Annotations
Loss function
Training

## Slide 11: III. Implemented architecture
Neural network
HRNet, one of the latest architecture in semantic key points detection
Excels in capturing the connections between local and global features
Outputs a Gaussian heatmap instead of coordinates
The output resolution is 4 times smaller on each dimension
Loss:

## Slide 12: III. Increase diversity in the images
Train set: 1,047 images
Test set 645 images
Synthetic data generation from images taken in front of a blue drape to generate data with diverse background
Classic data augmentation: rotation, brightness and contrast, flipping, etc.

## Slide 13: III. Postprocessing and confidence score
Coordinates are estimated from the argmax of the heatmap
The maximum value of the heatmap is a number between 0 and 1 and is used as a confidence score
A threshold can be used to discard images according to this confidence score

## Slide 14: III. 2D Key points detection results
Random test samples visualization
Test set metrics

## Slide 15: III. Qualitative analysis – Best samples

## Slide 16: III. Qualitative analysis – Worst samples

## Slide 17: IV. Triangulation through time

## Slide 18: IV. Triangulation pipeline
Projection pipeline
Triangulation pipeline

## Slide 19: IV. Mathematical details
Image coordinates
Unknown
Instrument tracker rotation and translattion
Unknown 3D transformation
Intrinsic matrix
Let’s note
Therefore
Last line is null so we have two constraining equations per image
For an ideal case,
Each image constrains the tip to be on a line in the 3D space
With more than 2 lines we can get the tip by optimizing the coordinates to match all lines

## Slide 20: IV. Results analysis
The more images the better
25 images after postprocessing yields an error of 3.0 mm
25 frames correspond to a video of 10 seconds

## Slide 21: V. How to get better?

## Slide 22: IV. Better annotations
Annotations are gathered from the previous calibation method which has an error up to 2 mm.
The projection error can go up to 5 pixels which might confuse the network during training
A series of experiments seem to point out that most of this error comes from the tracker’s positions

## Slide 23: IV. Architecture limitations
The output resolution of the network offers a maximum precision of +/- 1 pixel
The input image is a resized one because of hardware limitation during training (0.5 factor in average)
A second network could be trained to refine the predictions of the first one

## Slide 24: Thank you for your attention
Clement Wang
clementwang2001@gmail.com